## Slide 1: Lecture 2 — Energy generation
PHY199-RAP · Energy in the 21st Century Dr. Salvatore Rappoccio

## Slide 2: Electricity generation : The physics

## Slide 3: Turbines and Motors
Turbine:
  Fixed blades and rotating blades are inside a casing.
  The rotating blades are attached to a shaft, which is then connected to a wire that rotates inside a magnetic field.
  Steam passes through, turning the rotating blades and the shaft, generating electricity
https://www.turbinesinfo.com/steam-turbines/

## Slide 4: Circuits
Before we really understand power generation, we need to understand circuits
We’re go deeper into three concepts:
  Capacitance (C): stores energy in an electric field
  Inductance (L) : stores energy in a magnetic field
  Resistance (R) : dissipates thermal energy via heat

## Slide 5: Electricity
Teeny tiny bit of vector addition
The components of Coulomb’s law parallel to the plates CANCEL, the components perpendicular to the plates ADD, so you get a constant electric field
Why is this important?
  If you hook up a battery, this supplies a direct current electric field between the plates
Not responsible for this, just for enrichment
Now just draw a line to represent the charges, and you get a PARALLEL PLATE CAPACITOR

## Slide 6: Capacitance
If you put a positive and negative plate next to each other, it can store electric energy
This is called a “capacitor” and how much it can store is the “capacitance”
Voltage: Volts
Charge: Coulombs
Capacitance: 1 Farad = 1 Coulomb / Volt
You ARE responsible to understand capacitance is charge divided by voltage
https://en.wikipedia.org/wiki/Capacitor

## Slide 7: Induction
Mathematically:
  Electromotive force (voltage) is generated by changing magnetic field
Magnetic flux:
1 Weber =1 Tesla
Time:
seconds
Electromotive force (Voltage):
1 Volt
You ARE responsible to understand a voltage is induced from a changing magnetic flux

## Slide 8: Inductance
If you wrap a coil around something magnetic, it can store magnetic energy just like a capacitor stores electric energy
This is called an “inductor” and how much magnetic flux it stores is called the “inductance”
https://en.wikipedia.org/wiki/Inductor
Current: Amps
Flux: Tesla x Area
Inductance: 1 Henry = 1 Tesla x m2 / Amp
You ARE responsible to understand inductance is flux divided by current

## Slide 9: Resistance
Unfortunately, friction exists
The electrons flowing through the wires bump into other electrons in the metal, so you get RESISTANCE
Just like all resistance, it generates heat.
+
-
Resistance:
Ohms = volts per amp
Current:
Ampere = Coulombs / second
Electric potential:
Joules / Coulomb or VOLTS
You ARE responsible to understand that resistance is voltage divided by current

## Slide 10: RLC Circuits
What happens if you put a resistor, an inductor, and a capacitor in a circuit?
  Capacitance stores electric energy
  Inductor stores magnetic energy
  Resistor heats up (but is what we’re using for light bulbs, etc)

## Slide 11: RLC Circuits
This is a tough math problem so I’ll just quote the answer, but for the math nerds (like me) the derivation is on the side (it’s a second-order differential equation with damping!)
Current will follow a DAMPED COSINE WAVE:
https://en.wikipedia.org/wiki/RLC_circuit
Suppose V is constant, take derivatives and divide by L:
Second order differential equation! Solved with sine waves.
Current:
Amps
Initial current:
Amps
Base of Natural log
e = 2.71…
Cosine
Damping factor
Not responsible for this, just for enrichment
Frequency

## Slide 12: Current : Damped Cosine Wave
Cosine makes it wiggle at frequency f
Exponential decay
from dissipative losses
Initial current
You ARE responsible to understand that an RLC circuit wiggles at a specific frequency and decays over time due to dissipative losses.

## Slide 13: AC Current
This is an alternating current
The electrons in the material go back and forth, and can be used in powering circuits
https://www.build-electronic-circuits.com/difference-ac-vs-dc/

## Slide 14: Turbines and Motors
Turbine:
  Fixed blades and rotating blades are inside a casing.
  The rotating blades are attached to a shaft, which is then connected to a wire that rotates inside a magnetic field.
  Steam passes through, turning the rotating blades and the shaft, generating electricity
https://www.turbinesinfo.com/steam-turbines/

## Slide 15: AC vs DC
Turbines naturally produce AC power
To convert to DC, it’s necessary to make a commutator and use a dynamo that flips the sign every turn.
More on this later!
http://www.bigshotcamera.com/learn/power/dynamo
Flip - to +

## Slide 16: AC vs DC
Batteries were the first device used to generate power
Smaller scale, can apply directly to what you need
Batteries supply DC, so the first thoughts (Edison) were to use DC power
We’ll discuss the AC vs DC wars next class, but first let’s look at the science case

## Slide 17: Why AC won : Resistive Losses
Remember resistance!
Or rewrite the equation:
Power generated at the station is
But remember the power lost by a resistor is
Resistance is voltage over current
Voltage is current times resistance
Power lost scales like current SQUARED
Power generated is current times voltage

## Slide 18: Why AC Won: Transformers
Now for the big technological advantage of AC current
From Faraday’s law:
The ratio of voltages is:
https://en.wikipedia.org/wiki/Transformer
Not responsible for this, just for enrichment

## Slide 19: Why AC Won: Transformers
Transformers can STEP UP or STEP DOWN voltage
You ARE responsible to understand that you can use a transformer to step voltage up or down
Step down
Step up

## Slide 20: Tophat question
If you have a constant power source with , and the power lost has , is more power lost at high voltage, low voltage, or they are the same?
  A: More power lost at high voltage.
  B: More power lost at low voltage.
  C: The power losses are the same.

## Slide 21: Tophat question
If you have a constant power source with , and the power lost has , is more power lost at high voltage, low voltage, or they are the same?
  A: More power lost at high voltage.
  B: More power lost at low voltage.
  C: The power losses are the same.
You ARE responsible to understand / remember that for a constant power generated, there are more losses at low voltage than at high voltage

## Slide 22: Now You Understand The Grid
https://en.wikipedia.org/wiki/Electric_power_transmission

## Slide 23: To remember
Concept (need to remember) | Formula (for enrichment)
capacitance is charge divided by voltage | 
a voltage is induced from a changing magnetic flux | 
inductance is flux divided by current | 
resistance is voltage divided by current | 
Alternating current (AC) circuits wiggles at a specific frequency and decays over time due to dissipative losses. | 
you can use a transformer to step voltage up or down | 
for a constant power generated, there are more losses at low voltage than at high voltage | 
Concept (need to remember) | Formula (for enrichment)
capacitance is charge divided by voltage | 
a voltage is induced from a changing magnetic flux | 
inductance is flux divided by current | 
resistance is voltage divided by current | 
Alternating current (AC) circuits wiggles at a specific frequency and decays over time due to dissipative losses. | 
you can use a transformer to step voltage up or down | 
for a constant power generated, there are more losses at low voltage than at high voltage | 

## Slide 24: Links & References
References
Steam turbines
Capacitor
Inductor
RLC circuit
AC vs DC
Dynamo (BigShot)
Commutator
Dynamo (Wikipedia)
Transformer
Power transmission
Image credits (Wikimedia Commons)
Capacitor image 1
Capacitor image 2
Inductor image 1
Inductor image 2
Transformer image