## Slide 1
Lecture 2 — Magnetism
PHY199-RAP · Energy in the 21st Century
Dr. Salvatore Rappoccio
Notes: Companion to the electricity deck. We pick up exactly where the electricity lecture ended (P=VI, I^2R losses, the War of the Currents) and show how magnetism is what actually GENERATES and MOVES electricity. Magnitudes only — no vectors.

## Slide 2
1
MAGNETISM
The other half of electricity — and how we make it move

## Slide 3
2
Where we left off
In the electricity lecture we built up direct current (DC):
Current I — charges per second (amperes)
Voltage V — energy per charge that pushes them (volts)
Power P = V · I, and resistive loss P = I² · R
That last equation started the War of the Currents.
But one thing was missing: where does the voltage come from in the first place? Batteries and solar are DC — yet the whole grid runs on something else.
The answer is
MAGNETISM
Almost every electron on the grid was pushed by a magnet.
Notes: Callback slide. The electricity deck ended at I^2R and 'this sets up the War of the Currents.' Magnetism is the missing piece: it's the source of the EMF. Tease: batteries/solar are DC, but the grid is AC — why? Magnetism answers it.

## Slide 4
3
The magnetic field
Every magnet has two poles: North and South.
Like poles push apart; opposite poles pull together — just like electric charges.
A magnet fills the space around it with a magnetic field, B — the magnetic version of the electric field.
The field is strong near the poles and weakens with distance.
One weird rule: you can never get a single pole. Cut a magnet in half and each piece grows its own N and S.
Magnetic field B:
measured in Tesla (T)
N
S
Sources: Encyclopædia Britannica, “magnetism” & “magnetic field”; HyperPhysics (Georgia State University), Magnetic Field.
Notes: Keep it to magnitudes and pictures. Key intuitions: two poles, like repels/opposite attracts, field fills space and falls off with distance, no magnetic monopoles. Unit is the Tesla — a big unit: Earth's field is ~50 microtesla, a fridge magnet ~5 milliteslas, an MRI ~1.5-3 T.

## Slide 5
4
1820: Electricity IS magnetism
Hans Christian Ørsted was lecturing when he noticed a compass needle twitch every time he switched on a current.
An electric current creates a magnetic field around the wire.
Electricity and magnetism are not two subjects — they are one thing: electromagnetism.
Wrap the wire into a coil and the fields add up: you have built an electromagnet — a magnet you can switch on and off.
current
magnetic field circles the wire
This is the seed of every motor, generator, and transformer in this lecture.
Sources: Ørsted (1820), reported in Thomson's Annals of Philosophy; Encyclopædia Britannica, “Hans Christian Ørsted.”
Notes: The founding accident of E&M. Emphasize the unification: current -> magnetic field. Coil = electromagnet you can turn on/off, which is what makes controllable machines possible. This is the same Ørsted->Faraday->Maxwell chain named in the electricity deck.

## Slide 6
5
A magnet can push a current
Ørsted: a current makes a magnetic field. So a current-carrying wire is itself a little magnet.
Put that wire inside another magnet's field and the two fields push on each other — the wire feels a force.
Magnitude (no vectors): the force grows with the field, the current, and the length of wire in the field.
Force = B × I × L
(field × current × wire length)
Units: Tesla × Ampere × meter = Newton
N
S
wire (current)
force
You ARE responsible to understand that a magnetic field pushes on a current — this is how a motor works.
Source: HyperPhysics (Georgia State University), Magnetic Force on a Current-Carrying Wire.
Notes: This is the motor principle. Units check: T·A·m = N, so the salmon box ties back to the derive-your-units style of the electricity deck. Keep it magnitudes only.

## Slide 7
6
How a motor works
Bend the wire into a loop and place it between magnet poles.
Current up one side, down the other — so the two sides feel forces in opposite directions.
Opposite forces on opposite sides = a twist. The loop spins.
A switch (the commutator) flips the current each half-turn so it keeps spinning the same way.
Electrical energy → motion. Fans, drills, hard drives, electric cars, the pump on your furnace.
N
S
opposite forces → it spins
Source: HyperPhysics (Georgia State University), DC Motor; Encyclopædia Britannica, “electric motor.”
Notes: Motor = loop in a field + commutator. Electrical -> mechanical. Give everyday examples so first-years feel it's everywhere. We'll flip this exact machine around in two slides to make a generator.

## Slide 8
7
FARADAY’S LAW
The most important equation in this whole course

## Slide 9
8
First: magnetic flux
Flux is just “how much magnetic field passes through a loop.”
More field, or a bigger loop, means more flux through it.
Think of rain falling into a bucket: a stronger downpour, or a wider bucket, catches more.
Flux = B × A
(field × loop area)
Units: Tesla × meter² = Weber (Wb)
field B
loop, area A
Source: HyperPhysics (Georgia State University), Magnetic Flux.
Notes: Flux = B x A (magnitude, field perpendicular to the loop). The rain-in-a-bucket analogy makes it concrete. We only need flux so we can talk about it CHANGING on the next slide — that's Faraday.

## Slide 10
9
Faraday’s law (1831)
Ørsted: a current makes a magnetic field. Faraday asked the reverse — can a magnetic field make a current?
His answer: only if the flux is CHANGING.
A steady magnet next to a coil does nothing. Move it, and the changing flux pushes a voltage — an EMF — around the coil.
Faster change → bigger voltage. More turns of wire → bigger voltage.
Voltage = (change in flux) ÷ (change in time)
Units: Weber ÷ second = Volt
You ARE responsible: a CHANGING magnetic flux creates a voltage. This is how ALL electricity is generated.
N
move the magnet → voltage
Sources: Faraday, Experimental Researches in Electricity (1831–32); HyperPhysics (Georgia State University), Faraday's Law.
Notes: THE key slide. Units: Wb/s = V ties straight back to volts from the electricity deck. Emphasize 'changing' — a static field does nothing. Faster change and more turns => more voltage. Everything after this is applications of this one sentence.

## Slide 11
10
How do you change the flux?
Anything that changes B × A through the loop makes a voltage:
Move a magnet toward or away from the coil
Move the coil instead of the magnet
Change the strength of the field (e.g., ramp a current up and down)
Spin the loop so its face turns toward and away from the field
That last one — spinning a loop — is the entire electric-power industry.
Spin a loop in a magnet
→
you have a GENERATOR
Source: HyperPhysics (Georgia State University), Faraday's Law / Motional EMF.
Notes: Four ways to change flux; the fourth (rotating the loop) is the generator, which we build next. Foreshadow: this will be relevant for turbines and for AC.

## Slide 12
11
The generator: one machine
Spin a coil inside a magnet. As it turns, the flux through it rises and falls, so Faraday’s law pumps out a voltage.
This is a generator: motion → electricity. It is a motor run backwards.
Coal, gas, nuclear, hydro, wind, geothermal — underneath, every one of them is the SAME machine: something spins a magnet past a coil.
They differ only in what does the spinning. The physics of the last step is identical.
N
S
spin
voltage out (AC)
Source: HyperPhysics (Georgia State University), Electric Generator; Encyclopædia Britannica, “electric generator.”
Notes: The unifying idea of the course (echoes the electricity deck's 'every plant is one machine'). Coal/nuclear/gas/hydro/wind all just spin a magnet past a coil; only the energy source that does the spinning differs. Solar PV is the exception — no spinning — which is why it's DC, tie-in to earlier.

## Slide 13
12
What does the spinning? Turbines
A turbine is a fancy pinwheel: a fluid pushes angled blades on a shaft and the shaft spins.
That shaft turns the generator’s coil → Faraday’s law → electricity.
The whole chain:
heat / falling water / wind → spin turbine → spin coil in magnet → voltage → grid
Niagara Falls (from Lecture 1): gravity pulls water down → turbine → generator. Same last step as a coal plant, no carbon.
heat / water / wind
turbine spins
coil in magnet
voltage → grid
Source: HyperPhysics (Georgia State University); Encyclopædia Britannica, “turbine.”
Notes: Turbine = the thing that spins the generator. Callback to Niagara/hydro from Lecture 1 and the water-mill lineage from the electricity deck. Coal/nuclear boil water to make steam to spin it; hydro uses falling water; wind uses air. The generator step is always identical.

## Slide 14
13
Same machine, both directions
MOTOR
Put electricity IN
Field pushes the current
Get motion OUT
electricity → motion
GENERATOR
Put motion IN
Changing flux makes a voltage
Get electricity OUT
motion → electricity
An electric car uses this: motor to drive, generator to brake (regenerative braking recharges the battery).
Notes: The elegant symmetry: motor and generator are the same device. Regenerative braking in EVs is the everyday proof — the drive motor becomes a generator when you slow down.

## Slide 15
14
AC CURRENTS
Why the grid’s voltage goes up and down 60 times a second

## Slide 16
15
A spinning loop makes AC
As the loop spins, its face turns toward the field, then edge-on, then toward the other pole.
So the flux goes up, down, up, down — and by Faraday, the voltage does too.
The voltage smoothly swings positive, then negative, then positive: alternating current (AC).
AC isn’t a design choice — it’s what a rotating generator naturally produces.
Source: HyperPhysics (Georgia State University), AC Generator; Encyclopædia Britannica, “alternating current.”
Notes: Crucial 'aha': AC is not arbitrary. A rotating coil produces a sinusoidal voltage automatically. DC would actually require extra hardware (the commutator) to force it. This is half the reason AC won the War of the Currents.

## Slide 17
16
60 times a second
In North America the grid completes 60 full swings every second: 60 hertz (Hz).
Most of the rest of the world uses 50 Hz. Neither is “right” — they’re just standards everyone agreed to keep in step.
Every generator on the grid must spin in lockstep at that frequency, or the system tears itself apart.
Your wall outlet: about 120 volts, alternating at 60 Hz.
USA
60 Hz
≈ 120 V
We’ll come back to keeping the whole grid in sync when we talk about blackouts.
Sources: Encyclopædia Britannica, “alternating current”; NYISO (grid frequency operations).
Notes: 60 Hz US / 50 Hz much of the world — arbitrary standards. All generators must stay phase-locked. 120 V wall outlet at 60 Hz. Forward-reference to the grid/blackout material in the main lecture.

## Slide 18
17
THE AMPÈRE–MAXWELL LAW
Finishing the loop between electricity and magnetism

## Slide 19
18
Ampère: how much field?
Ørsted showed a current makes a magnetic field. André-Marie Ampère measured how much.
Around a straight wire: more current makes a stronger field; the field weakens as you move away.
Coil the wire tightly (a solenoid) and the field inside adds up into a strong, uniform electromagnet.
field ∝ current ÷ distance from the wire
Not responsible for this, just for enrichment
strong uniform field inside a coil
Source: HyperPhysics (Georgia State University), Ampère's Law / Solenoid; Encyclopædia Britannica, “André-Marie Ampère.”
Notes: Ampère quantifies Ørsted: B grows with current, falls with distance. Solenoid = coil that concentrates the field. Keep the proportionality qualitative (magnitudes/scaling only). This is 'enrichment' depth.

## Slide 20
19
Maxwell’s twist (1865)
Faraday: a changing magnetic field makes an electric voltage.
Maxwell added the mirror image: a changing electric field makes a magnetic field.
Now they feed each other: a changing E makes a B, whose change makes an E, and off it goes — a self-sustaining wave that needs no wire and no medium.
Maxwell computed its speed and got 300,000 km/s — the speed of light. Light is an electromagnetic wave.
speed of light
c ≈ 3 × 10⁸ m/s
E and B waves make each other
Radio, Wi-Fi, microwaves, X-rays, the warmth of the sun — all the same wave, different frequency.
Sources: Maxwell, “A Dynamical Theory of the Electromagnetic Field” (1865); HyperPhysics (Georgia State University), Electromagnetic Waves.
Notes: Faraday + Maxwell together close the loop and predict light. Keep it conceptual — no wave equations. The payoff line: everything from radio to sunlight is the same phenomenon. This is the intellectual summit of classical physics; deliver it with a bit of awe.

## Slide 21
20
TRANSFORMERS
Faraday’s law again — and the reason the grid is AC

## Slide 22
21
How a transformer works
Two coils share the same iron core. AC in the first coil makes a constantly changing flux.
That changing flux runs through the second coil, so — Faraday again — it develops its own voltage.
The voltage ratio equals the ratio of turns of wire:
out ÷ in = (turns out) ÷ (turns in)
More turns out → step UP the voltage
Fewer turns out → step DOWN
Catch: it only works if the flux keeps CHANGING — so transformers work on AC, not DC.
iron core
AC in
voltage out
Source: HyperPhysics (Georgia State University), Transformer; Encyclopædia Britannica, “transformer.”
Notes: Transformer = two coils, one core, Faraday's law. Turns ratio sets voltage ratio. The killer point: it needs CHANGING flux, so it only works with AC. This is the hinge of the whole War of the Currents argument on the next slide.

## Slide 23
22
Why AC won the War
Remember the loss equation from the electricity lecture: P = I² × R.
Loss grows with the current SQUARED. Halve the current and you cut losses to a quarter.
But power delivered is P = V × I. To move the same power with less current, you must raise the voltage.
Transformers let you step voltage way UP for the long trip, then back DOWN for your house — but only with AC.
That is why the grid is AC. Tesla and Westinghouse’s AC beat Edison’s DC because DC couldn’t be transformed.
Generator
~ thousands of V
Step UP
hundreds of kV
Long lines
low current, low loss
Step DOWN
~120 V
Your house
Sources: HyperPhysics (Georgia State University), Power Transmission; Encyclopædia Britannica, “War of the Currents.”
Notes: The synthesis. I^2R (from the electricity deck) + transformers (this deck) = why the grid is AC. High-voltage/low-current transmission minimizes I^2R loss; transformers make voltage conversion trivial, and they only work on AC. Sets up the AC/DC 'Current Wars' politics in Week 3.

## Slide 24
23
Where I live: inside a magnet
I work on the CMS experiment at CERN’s Large Hadron Collider.
CMS stands for Compact Muon Solenoid — the “S” is a magnet: one of the most powerful superconducting solenoids ever built.
Its field is about 3.8 tesla — roughly 100,000× Earth’s magnetic field.
That field bends the paths of particles from proton collisions so we can measure them — the same magnetic force on a current, just aimed at the fundamental building blocks of matter.
Same physics as your ceiling fan. Different stakes.
CMS solenoid
3.8 T
Source: CERN, CMS experiment technical documentation (magnet system).
Notes: Authentic Sal tie-in (per project style notes: lean into CMS/CERN). The magnet is literally in the name. 3.8 T ~ 100,000x Earth's ~50 microtesla field. Same 'force on a current' physics as the motor slide, applied to particle tracking. Keep it warm and a little funny.

## Slide 25
24
To remember
A current makes a magnetic field (Ørsted); a magnetic field pushes on a current (that’s a motor).
Faraday’s law: a CHANGING magnetic flux creates a voltage. This is how all electricity is generated.
A generator is a coil spun in a magnet; a turbine is what spins it. Every power plant shares this last step.
A spinning generator naturally makes AC — in the US, 60 Hz at ~120 V.
Ampère–Maxwell: changing electric and magnetic fields make each other — and that wave is light.
A transformer changes AC voltage using the turns ratio — and this is why the grid is AC.
Notes: Six takeaways, matching the electricity deck's 'To remember' closer. These are the responsible-for items. Faraday's law is the one they must not forget.

## Slide 26
25
Sources & references
Primary sources Ørsted (1820) · Faraday (1831–32) · Maxwell (1865)
HyperPhysics (Georgia State Univ.) magnetic field · force on wire · DC motor · magnetic flux · Faraday's law · motional EMF · generator · AC generator · solenoid · Ampère's law · EM waves · transformer · power distribution
Encyclopædia Britannica magnetism · magnetic field · Ørsted · electric motor · electric generator · turbine · alternating current · transformer · Ampère
Also cited Current Wars · CMS solenoid · NYISO
Vetted video explainers 3Blue1Brown · Veritasium · Practical Engineering · particleclara · CERN CMS · Brian Cox
Every underlined item links to its source. Physics here is settled textbook material; no federal (.gov) source relied upon.
Notes: Complete reference list. Every reference cited on a slide appears here as a clickable link (1–3 word anchors), grouped by source: primary sources, HyperPhysics topic pages, Britannica topic pages, other cited items (War of the Currents, CMS solenoid, NYISO), and the vetted video creators from the project's trusted list. Confirm creator/video URLs still resolve before class.