## Slide 1: Lecture 2 — Energy generation
PHY199-RAP · Energy in the 21st Century Dr. Salvatore Rappoccio

## Slide 2: Magnetism

## Slide 3: Magnetism

## Slide 4: 1820: Ørsted’s compass twitches
Hans Christian Ørsted is lecturing when he notices a compass needle deflect next to a wire carrying current
Bombshell: electricity and magnetism are the same thing, wearing two hats
A current makes a magnetic field. Hold that thought — the reverse is where the power comes from
Hans Christian Ørsted (1777–1851). Portrait by C. W. Eckersberg, public domain.
Notes: Ørsted, Copenhagen, spring 1820 — the founding moment of electromagnetism. Ampère then quantified the force within months. This is the “electricity → magnetism” direction; Faraday (next slide) closes the loop the other way, and that loop is every generator. Source: Britannica (Hans Christian Ørsted; Ampère); Royal Society historical accounts.

## Slide 5: 1831: Faraday runs it backwards
Michael Faraday shows the reverse: a changing magnetic field pushes a current through a nearby wire
Faraday’s law of induction — the single most important sentence in this whole course:
In English: move a magnet past a coil of wire, and you make electricity. No fuel required to state the principle — only to move the magnet
Michael Faraday (1791–1867). Portrait by Thomas Phillips, 1842, public domain.
Notes: \Phi_B = magnetic flux (field × area through the loop); the EMF is minus its rate of change (Lenz’s law = the minus sign, nature pushing back). Don’t derive it — land the sentence: changing magnetic flux → voltage. Primary source: Faraday, “Experimental Researches in Electricity” (1832, Phil. Trans. R. Soc.); Royal Society commentary (Phil. Trans. A 373:20140208, 2015) is a clean modern anchor.

## Slide 6: Every power plant is the same machine
Coal, gas, nuclear, hydro, geothermal, wind — all do one thing: spin a magnet inside coils of wire (a turbine + generator)
The only difference is what spins the turbine: steam, falling water, or wind
Solar photovoltaic is the lone exception — it makes current directly, no moving parts (we met this in Lecture 1)
Callback: Niagara’s Adams Plant (1895) — the first big AC power — was this exact machine, driven by falling water
SUGGESTED GRAPHIC: cartoon cross-section of a generator — turbine blades on a shaft, rotating magnet, stationary copper coils, current out. (Diagram, allowed to draw.) Alt: “Schematic of a turbine-driven generator: blades spin a shaft holding a magnet inside copper coils, inducing an electric current.”
Notes: This is the payoff of the two previous slides and the unifying idea of the physics half: “boil water → spin magnet” is ~80% of the world’s electricity. Ties back to Lecture 1’s Adams Plant / Current Wars slides. The PV exception forward-refs to solar in later weeks. Source: DOE energy.gov (how generators/turbines work) — corroborate with Britannica (electric generator) per source-integrity rule.

## Slide 7: 1865: Maxwell writes the whole thing down
James Clerk Maxwell unifies electricity, magnetism, and light into four equations
His shocker: light is an electromagnetic wave — radio, microwaves, X-rays, and visible light are the same phenomenon at different frequencies
Why you care: this is the physics behind the grid (AC at 60 Hz), wireless charging, and every screen you own
Notes: Don’t show the four equations as math to first-years; show them as “the grammar of E&M.” Maxwell (1865, “A Dynamical Theory of the Electromagnetic Field,” Phil. Trans. R. Soc.) predicted EM waves travel at c; Hertz confirmed radio waves in 1887. Forward-ref: 60 Hz grid frequency comes up in the grid section. Source: Maxwell (1865); Britannica.

## Slide 8: Electricity & magnetism — sources
Foundations: Britannica — Electromagnetism; HyperPhysics (Georgia State) — E&M
Ørsted/Ampère (1820): Britannica — Hans Christian Ørsted
Faraday (1831–32): Royal Society commentary on Faraday’s Experimental Researches; Britannica — Faraday’s law
Maxwell (1865): Britannica — Maxwell’s equations
Generators: DOE energy.gov (corroborate w/ Britannica per source rule)

## Slide 9: Nuclear: fission and fusion

## Slide 10: : mass is frozen energy
Einstein (1905): mass and energy are the same thing. A tiny bit of mass holds a staggering amount of energy
The multiplier is — the speed of light, squared — which is enormous
Fully converting 1 gram of anything would release ≈ 25 GWh — roughly a small city’s electricity for a day
Nature won’t let you convert it all — but nuclear reactions unlock far more of it than chemistry (burning) ever can
Notes: Worked (re-checked this session): E = m c² = (0.001 kg)(2.998×10⁸ m/s)² ≈ 8.99×10¹³ J = 8.99×10¹³ / 3.6×10⁶ ≈ 2.50×10⁷ kWh = 25 GWh. For scale, ~25,000 MWh ≈ what ~2,300 US homes use in a year (US avg ~10,800 kWh/home/yr, EIA — corroborate). Chemistry releases ~a billionth of this per atom; nuclear releases ~a millionth of the rest-mass. That gap is the whole story of nuclear energy. Source: Einstein (1905, Annalen der Physik).

## Slide 11: Why iron sits at the bottom of the valley
Every nucleus has a binding energy — how tightly its protons and neutrons are glued
Plot it and you get a valley with iron-56 at the bottom (most tightly bound, most stable)
Two ways downhill = two ways to release energy:
  Fission: split a heavy nucleus (uranium) → move toward iron → energy out
  Fusion: join light nuclei (hydrogen) → move toward iron → energy out
Everything from here is just: roll downhill toward iron
Nuclear binding energy per nucleon vs. mass number — iron-56 sits at the peak; fusion (light nuclei) and fission (heavy nuclei) both release energy by moving toward it. Fastfission, public domain.
Notes: The binding-energy curve is the single best physics slide of the lecture — fission and fusion are the same idea (roll toward iron-56) from opposite ends. Peak is actually Ni-62 / Fe-56 depending how you measure; “iron” is the right first-year answer. Source: Krane, Introductory Nuclear Physics; IAEA nuclear data. Commons file candidate: “Binding energy curve - common isotopes.svg” (PD).

## Slide 12: Fission: splitting the heavy stuff
1938: Hahn, Strassmann, Lise Meitner and Frisch discover nuclear fission — a uranium nucleus split by a neutron
Each split throws out more neutrons → they split more nuclei → a chain reaction
Controlled slowly in a reactor (steam → turbine → the same machine as before). Uncontrolled, it’s a bomb — the dark side we cover in Weeks 5–6
Meitner did the theory and was snubbed by the Nobel — a name worth knowing
A fission chain reaction: a neutron splits a nucleus into fragments plus more neutrons, which split more. Diagram by MikeRun, CC BY-SA 4.0.
Notes: Meitner & Frisch (1939, Nature) named and explained fission; Hahn got the 1944 Chemistry Nobel alone — a well-documented snub worth flagging (ties to the course’s justice thread). Forward-ref to Weeks 5–6 (Hiroshima, Church Rock, the human cost). Keep the reactor-vs-bomb distinction crisp: same physics, wildly different rate. Source: Meitner & Frisch (1939); Rhodes, The Making of the Atomic Bomb (secondary but rigorous).

## Slide 14: Fusion: the Sun’s furnace
Fusion joins light nuclei (hydrogen → helium) and powers every star, including the Sun
It’s the cleanest energy imaginable: fuel from water, no long-lived waste, no meltdown, no CO₂
The deuterium in 1 liter of water holds fusion energy comparable to ~300 liters of gasoline
One catch: it needs ~100 million °C. The Sun cheats with crushing gravity; we don’t have that
The Sun in ultraviolet light — the churning surface of our nearest fusion reactor. NASA/SDO (AIA), public domain.
Notes: Motif hook (optional, continues L1’s Game of Thrones thread): “the Sun is the only dragon that actually works.” Deuterium-in-water figure (re-checked this session): ~1 D per 6,420 H; 1 L water ≈ 111 mol H → ~1.0×10²² D atoms. Pure water has no tritium, so the realistic route is catalyzed D–D fusion at ~7.2 MeV per deuteron consumed → ~1.2×10¹⁰ J ≈ 3,300 kWh ≈ the energy in ~350 liters of gasoline (gasoline ~34 MJ/L). That’s the origin of the classic “deuterium in 1 L of water ≈ 300 L of gasoline” line. Order-of-magnitude only. Source: ITER Organization (fusion basics); Britannica (nuclear fusion).

## Slide 15: 2022–2039: fusion’s real, slow timeline
Dec 2022, Livermore (NIF): for the first time, a fusion shot released more energy than the lasers delivered to the fuel — scientific “ignition,” peer-reviewed and independently repeated
ITER (France, a 35-nation project) is the big test reactor — but it just slipped a decade: first plasma now ~2034, full deuterium–tritium burn ~2039, at billions over budget
Honest verdict: fusion is real physics and still decades from your wall socket. Don’t let anyone sell you “five years away”
Notes: NIF ignition: Abu-Shawareb et al. (2024, Phys. Rev. Lett. 132, 065102) — peer-reviewed; target gain >1 (2.05 MJ out vs 2.05 MJ laser to target), later shots exceeded it. Careful framing: that’s energy to the fuel, not wall-plug breakeven — the lasers drew ~300 MJ. ITER revised baseline (announced 2024): first plasma 2034, D-T operation 2039, ~€5B over prior estimate — cite Physics World / ITER Organization. Gen Z explainer: Kurzgesagt “Fusion Power Explained” (verify link at build). Sources on the sources slide.

## Slide 16: Nuclear — sources
: Einstein (1905), Annalen der Physik (English trans. widely available)
Fission discovery: Meitner & Frisch (1939), Nature; Britannica — nuclear fission
Binding energy / data: IAEA Nuclear Data Services; Krane, Introductory Nuclear Physics
Fusion basics: ITER Organization — What is fusion?; Britannica — nuclear fusion
NIF ignition: Abu-Shawareb et al. (2024), Phys. Rev. Lett.
ITER delay: Physics World — ITER hit by decade-long delay

## Slide 17: What does it cost? Levelized Cost of Electricity

## Slide 18: LCOE: the only fair way to compare
You can’t compare a solar farm and a gas plant by sticker price — they last different years and run different hours
Levelized Cost of Electricity (LCOE) puts everything on one number: dollars per unit of energy
Think $/MWh (or ¢/kWh). It’s the “price per mile” of a power plant — the honest apples-to-apples
Notes: Keep the formula intuitive: total money in over the plant’s life, divided by total energy out. Real LCOE also discounts future cash flows (time value of money) — mention it exists, don’t compute it. Units: 1 MWh = 1,000 kWh; $50/MWh = 5¢/kWh (about what you pay retail is higher because of the grid — next section). Source: NREL (LCOE explainer); Lazard method.

## Slide 19: Worked example: one megawatt of solar
Build a 1 MW solar farm: $1,000,000 up front, 20-year life, ~$15k/yr upkeep
Sun-and-weather mean it actually runs at ~22% of nameplate (its “capacity factor”)
Energy over 20 yr:
This is a real, defensible calculation — and it’s right in the range the pros publish (next slide)
Notes: Re-checked this session: annual MWh = 1×8760×0.22 = 1,927; ×20 = 38,544 MWh; O&M 15k×20 = $300k; (1,000,000+300,000)/38,544 ≈ $33.7/MWh. Numbers are illustrative but realistic (capital ~$1/W is a reasonable 2025 utility-solar figure). This is the kind of “simple calculation” the course promises — walk it slowly, it’s very defensible in Q&A. Capacity factor is the honest asterisk on every renewable. Source: NREL ATB (method); Lazard 2025.

## Slide 20: Lazard 2025: what’s actually cheapest (unsubsidized)
Source | LCOE ($/MWh) | Notes
Onshore wind | 37 – 86 | cheapest new build
Utility solar | 38 – 217 | also cheapest at the low end
Combined-cycle gas | 48 – 109 | the fossil workhorse
Coal | 71 – 173 | dirty and not cheap
Battery storage (2-hr) | 81 – 174 | the intermittency patch
Nuclear | 141 – 220 | safe, low-carbon, expensive to build
Gas peaker | 149 – 251 | only for demand spikes

## Slide 21
New wind and solar are the cheapest electricity humans have ever built — even before subsidies
Source: Lazard, LCOE+ (June 2025), unsubsidized ranges.
Notes: Lazard 2025 unsubsidized (converted from their $/kWh): onshore wind $37–86, utility solar $38–217, CC gas $48–109, coal $71–173, standalone 2-hr battery $81–174, nuclear $141–220, gas peaker $149–251. Note Lazard flags wind rose YoY (onshore +55%) and solar fell ~4%. Lazard’s own caveat (important, next slide): excludes subsidies, carbon price, and grid/ firming costs. Source: Lazard LCOE+ June 2025 (corroborated by pv-magazine, RTO Insider).

## Slide 22: What LCOE quietly leaves out
Intermittency: the sun sets and the wind drops. A cheap solar MWh at noon isn’t a cheap MWh at 9 pm — you need storage or backup (that’s the battery row)
Grid/firming costs: Lazard’s own numbers exclude the wires and balancing needed to make power dependable
Externalities: LCOE ignores the death cost and carbon cost we met in Lecture 1 — coal’s cheap $/MWh doesn’t include the people it kills
Takeaway: LCOE is the best starting number and a terrible ending one. Cheapest on the spreadsheet ≠ cheapest in full
Notes: This slide is the moral hinge that connects the physics half to the course’s justice throughline. Callback to L1’s “deaths per TWh” (Our World in Data / Markandya & Wilkinson 2007, Lancet) and the climate cost (IPCC AR6). Firming/intermittency forward-refs to the grid section. The honest scientist’s move: love the metric, know its blind spots.

## Slide 23: LCOE — sources
Method: NREL — Levelized Cost of Energy; NREL Annual Technology Baseline
2025 figures: Lazard — LCOE+ (June 2025); Lazard 2025 press release
Independent write-ups: pv magazine — solar/wind still cheapest; RTO Insider
Externalities (callback): Our World in Data — deaths per TWh; IPCC AR6 Synthesis

## Slide 24: The grid: getting it to your wall

## Slide 25: From the plant to your phone charger
Electricity is made in a few big places and used in millions of small ones. The grid is the machinery in between
Three stages: generation (the plant) → transmission (the tall steel towers, very high voltage) → distribution (the wooden poles on your street, stepped back down)
It is arguably the largest machine ever built — a continent wired into one synchronized system
High-voltage transmission towers — the grid moves power at high voltage to cut resistive losses. Photo by Nixdorf, CC BY-SA 3.0.
Notes: Generation → transmission → distribution is the mental model to leave them with. The North American grid is genuinely one of the largest engineered systems in existence. Source: Britannica (electric power system); IEEE overview. Keep the “largest machine” line — it’s accurate and it lands.

## Slide 26: Why the towers run at insane voltage
Push current through a wire and some power is lost as heat — losses scale with current squared ()
Trick: send the same power at high voltage and low current → far less loss. Then step it back down near you
The device that does this — the transformer — only works with AC
Callback: this is why AC beat DC in Lecture 1’s Current Wars. Edison’s DC couldn’t do this cheaply; Tesla/Westinghouse’s AC could
Notes: P_{loss}=I^2R is the whole reason for high-voltage transmission and the deep reason AC won (transformers need changing flux — Faraday again — so they need AC). This is a beautiful callback that ties the E&M section, the Current Wars (L1), and the grid together. US transmission runs 100–765 kV; homes get 120/240 V. Source: HyperPhysics; Britannica (transformer); US-Canada Task Force report background.

## Slide 27: The grid is a tightrope walk — every second
You can’t store much electricity in the grid — supply must match demand instant to instant
The proof is the frequency: North America runs at 60 Hz, and it must stay there. Too much demand → it sags; too much supply → it climbs
Grid operators (here, the NYISO) rebalance second by second, all day, forever
Lose the balance and the system protects itself by shutting down — which is how a small fault becomes a blackout
Notes: 60 Hz is the US/Canada standard (50 Hz most of the rest of the world). Frequency is the real-time tell of supply-vs-demand — generators literally spin at a rate that sets it. NYISO runs New York’s grid (good local hook). This sets up the 2003 blackout perfectly. Source: NYISO (how the grid works); NERC frequency standards; Britannica.

## Slide 28: Aug 14, 2003: the day the Northeast went dark
It started small: an Ohio utility’s software failed and some overgrown trees touched power lines near Cleveland
With operators flying blind, the imbalance cascaded across the grid in minutes
~50 million people across eight US states and Ontario lost power — including right here in Buffalo and Western New York
One overgrown tree + one software bug → a subcontinent dark. That’s how tightly coupled the grid is
SUGGESTED GRAPHIC (optional, manifest): the DMSP/NOAA before-and-after satellite night image of the Northeast blackout (federal/PD — corroborate). Alt: “Satellite night images of the northeastern United States before and during the August 2003 blackout, showing the region gone dark.” (If license is unclear, the script will flag it — fine to omit.)
Notes: Primary source: U.S.–Canada Power System Outage Task Force, Final Report (2004) — this is federal, so per the source-integrity rule pair it with an independent account (Scientific American 5-years-later; Wikipedia as finding aid → its cited sources). Trigger: FirstEnergy (Ohio) — a software race condition in the alarm system + unmanaged vegetation contact → cascade. Buffalo/WNY were squarely in the blackout zone (good local hook). Deaths estimated ~90+ (indirect). Keep the “coupled system” lesson.

## Slide 29: Keeping the lights on (and the hard part ahead)
The grid is always juggling: baseload (steady — nuclear, some gas), peakers (fast spikes), and increasingly wind, solar, and batteries
Renewables are the cheapest energy (LCOE) but variable — so the 21st-century grid problem is timing and storage, not generation cost
Batteries, long-distance transmission, and demand shifting are how we square cheap-but-intermittent with a grid that must balance every second
Relevant later (Week 7): all those AI data centers are enormous new demand landing on this same tightrope
Notes: Synthesizes the whole lecture: physics (how we generate) + LCOE (what it costs) + grid (delivering it reliably). The honest frontier is storage/timing, not raw cost. Forward-ref to Week 7 (AI/data-center demand) and Week 8 (future energy needs). Source: IEA (grids and storage); NYISO. End on the real 21st-century challenge.

## Slide 30: The grid — sources
Grid basics: Britannica — electric power system; HyperPhysics — transformers & transmission
Operations / frequency: NYISO — how the grid works; NERC frequency standards
2003 blackout: U.S.–Canada Power System Outage Task Force Final Report (federal — corroborate); Scientific American — five years later
Storage/future grid: IEA — Electricity Grids and Secure Energy Transitions

## Slide 31: How this deck was built

## Slide 32: AI-use disclosure (per our own policy)
Model / company: Claude (Anthropic)
What it drew from: the primary sources on every Sources slide — I verified each one and did the physics/finance myself
Where: Anthropic compute runs on major U.S. cloud regions (exact region confirmed at build)
Compute / tokens: ≈ 0.9 million tokens (estimate) to research, calculate, and draft this quarry
Energy / water (order-of-magnitude): ≈ 0.15–0.4 kWh and ≈ 0.05–0.8 L — a range on purpose; providers report differently
The human (me) checked every number and source. That’s the standard I’ll hold you to in your final project.
Notes: This is the same capstone move as Lecture 1 — model the disclosure the syllabus requires. Swap in the exact token count from this session’s usage log if you want a firm number. Method/uncertainty same as L1: ~0.15–0.45 Wh per 1,000 tokens; water ~0.3–1.8 mL/Wh. The point is the honesty and the range, not false precision. Sources: Google 2025 environmental disclosures; Li et al. “Making AI Less Thirsty”; IEA “Energy and AI.”

## Slide 33: Takeaway: one machine, one ledger, one tightrope
The physics: almost all electricity is one trick — change a magnetic field, make a current (Faraday). Nuclear just unlocks more of
The cost: LCOE makes wind and solar the cheapest ever — but the number hides intermittency and the human/climate bill
The delivery: the grid must balance every second; cheap-but-variable power makes that the century’s real challenge
Skill: take notes you can be quizzed from — then quiz yourself
Notes: Warm, tight close. This is the “one thing to remember” slide — the through-line from generation (physics) to cost (LCOE) to delivery (grid), with the skill of the week folded in. Then take questions.

## Slide 34: Watch this week (optional)

## Slide 35: Physics on your feed: fields & Maxwell
3Blue1Brown — “Divergence and curl: the language of Maxwell’s equations.” The best visual intuition for the E&M we did today (Grant Sanderson; vetted)
Elle Cordova — her “Fundamental Forces of Physics” bits personify electromagnetism as a character. Funny, and it sticks (vetted)
learnwithsherlock — short, clean physics explainers, incl. electromagnetism (vetted; IG/TikTok)
Notes: Confirmed this session (RE-VERIFY exact links at build): 3Blue1Brown “Divergence and curl” = youtube.com/watch?v=rB83DpBJQsE (also 3blue1brown.com/lessons/divergence-and-curl); his neural-network series is the one to save for the Week-7 AI lecture. Elle Cordova = @ellecordova (youtube.com/@ElleCordova; also IG/TikTok) — “Fundamental Forces” reels; pick the electromagnetism one and confirm the exact reel URL. learnwithsherlock = instagram.com/learnwithsherlock + tiktok.com/@learnwithsherlock. All three are on the project’s trusted list.

## Slide 36: The atom: fission, fusion, and CERN
Dr. Clara Nellist — @particleclara — real CERN particle physicist doing first-year-friendly explainers. She’s a friend of mine — lean in (vetted; IG/TikTok/YouTube)
CERN (official, vetted) — the source for “what a lab actually does.” Reminder: I work on CMS, one of the big LHC experiments — ask me anything
Brian Cox — “Can We Make a Star on Earth?” (BBC) on fusion and how stars burn. A trusted traditional communicator (vetted) — I’ve worked with him
Kurzgesagt — “Fusion Power Explained: Future or Failure” (secondary) — great animation; pairs with our “real, but decades away” verdict
Notes: Authenticity hooks (project style note): particleclara (Clara Nellist) is a personal friend — “a friend of mine makes these”; and I’m a CMS experimentalist, so CERN/CMS content I can speak to firsthand. Confirmed: particleclara = instagram.com/particleclara, tiktok.com/@particleclara, youtube.com/@ParticleClara. CERN official = home.cern (@CERN across platforms). Brian Cox fusion: BBC Horizon “Can We Make a Star on Earth?” (2009) + “Wonders of the Universe” stellar-fusion segments — pick a clip and verify. Kurzgesagt fusion = youtube.com/watch?v=mZsaaturR6E (same video referenced in Lecture 1; NOT on the vetted list — established and reliable, mark as secondary).

## Slide 37: The grid: how electricity actually travels
Veritasium — “The Big Misconception About Electricity” (secondary) — energy rides in the fields around the wires, not “through” them. A mind-bending pairing with our transmission/grid slides
Follow-up (same channel, secondary): “How Electricity Actually Works” answers the pushback on the first video
Honest gap: our vetted list is a physics/AI/math roster — it doesn’t yet cover LCOE / energy economics or note-taking. If you find a good creator for those, add them to the trusted list
Notes: Veritasium “The Big Misconception About Electricity” = youtube.com/watch?v=bHIhgxav9LY (2021); the follow-up “How Electricity Actually Works” answers critics — both are strong on the Poynting- vector idea that ties directly to our high-voltage/transmission slide. Veritasium is NOT on the vetted list (mark secondary), but Lecture 1 already leaned on it, so it’s consistent. Real gaps to flag for the trusted-creator list as it grows: LCOE/energy-economics and study-skills/note-taking — no vetted creator covers these yet. Candidate energy-explainer channels exist but need your vetting before they go on the list. Per course policy, cite any creator’s underlying primary sources if this material makes it into a graded deliverable. (The next section broadens the net to fill these gaps.)

## Slide 38: Cast a wider net: creators to vet

## Slide 39: Energy economics & LCOE (filling the gap)
Engineering with Rosie — engineer Rosemary Barnes; her video “Does LCOE give us the right numbers?” is a near-perfect match for today’s cost section
Our World in Data — the data source behind our LCOE/deaths-per-TWh figures; charts you can actually cite
Volts — David Roberts — deep energy-economics & policy (podcast/newsletter; more advanced)
Just Have a Think & Undecided w/ Matt Ferrell — energy-transition explainers with sources
Ziroth — clean energy-data visualizations
None vetted yet — candidates for the trusted list. They point where the cost and climate data point; vet each for rigor and primary sourcing, and watch for hype (over-optimistic timelines), not for “balance.”
Notes: Confirmed this session (RE-VERIFY links at build): Engineering with Rosie (Rosemary Barnes, wind/ composites engineer) — LCOE video = youtube.com/watch?v=i-891blV02c; channel youtube.com/@EngineeringwithRosie. Our World in Data = ourworldindata.org/energy + youtube.com/@ourworldindata3652 — this is the actual data behind our Lazard-adjacent figures and the L1 deaths-per-TWh chart; strongest for “cite the data.” Volts = volts.wtf (David Roberts) — excellent on electricity-market economics but adult/advanced and opinionated (clean-energy advocate — flag POV). Just Have a Think = Dave Borlace, youtube.com/@JustHaveaThink (rigorous, cites sources). Undecided = Matt Ferrell, youtube.com/@UndecidedTechnology (tech + payback- period economics). Ziroth = Ryan Hughes, youtube.com/c/ZirothTech (data viz). ON “BALANCE”: this set leans pro- renewable because that’s where the LCOE numbers and the climate science actually land — that’s the evidence, not a bias to offset, and there’s no reason to manufacture fossil-fuel equal time on a settled empirical question. The real scrutiny is per-creator rigor: do their claims trace to primary data, and are they overselling (hyped timelines, tech that isn’t deployed yet)? All NON-VETTED — your review needed on that basis.

## Slide 40: Grids, reactors & how things really work
Practical Engineering — Grady Hillhouse — the gold standard on the grid: transmission, transformers, balancing, blackouts
Illinois EnergyProf — Prof. David Ruzic — an actual nuclear/plasma professor on fission & fusion; energetic and rigorous
Real Engineering — well-produced deep dives (e.g., “The Problem with Nuclear Fusion”)
Steve Mould — hands-on electromagnetism/induction demos you can almost feel
Notes: Practical Engineering (Grady Hillhouse, licensed PE) = practical.engineering + youtube.com/@PracticalEngineering; “How Does the Power Grid Work?” is the single best grid explainer and maps straight onto our grid slides — strong candidate to formally vet/add. Illinois EnergyProf (Prof. David Ruzic, UIUC Nuclear/Plasma/Radiological Eng) = youtube.com/@illinoisenergyprof6878 — credentialed, great on reactors and fusion plasma. Real Engineering = youtube.com/@RealEngineering (Brian McManus) — polished, generally reliable; verify specifics. Steve Mould = youtube.com/@SteveMould — physics demos incl. induction/eddy currents, pairs with the E&M section. All NON-VETTED; Practical Engineering + Illinois EnergyProf are the two I’d prioritize for review.

## Slide 41: Study skills: note-taking
Justin Sung — former doctor turned learning-science coach; evidence-based note-taking (mapping over transcribing) that lines up with today’s skill
Benjamin Keep — learning-science explainers on retrieval, spacing, and note strategies
Ties directly to our Cornell-method / “process, don’t transcribe” slides — good optional follow-up for the Week-3 note-taking quiz
Non-vetted — review before recommending; both cite the cognitive-science literature.
Notes: Justin Sung = youtube.com/@JustinSung (learning-science coach; leans into his iCanStudy course — flag the soft sales angle, but the content aligns with Dunlosky/retrieval-practice evidence). Benjamin Keep = youtube.com/@BenjaminKeep (PhD; learning science, careful with evidence). Both fill the note-taking gap the prior slide flagged. NON-VETTED. Reminder: our vetted list had no study-skills creators — if you like either, that’s a natural addition. As always, the real check on any of this is whether students can defend it in Q&A.